## Slide 1: Smart Irrigation System (Basic prototype)
By Samuel Batchelor

## Slide 2: Purpose of the Project
To create a smart watering system for the (lots) of plants in my garden
Monitor their environment
  How often they are being watered
  How warm and humid their environment is
  Know when they need to be watered
  Tracking their watering frequency

## Slide 3: Why
Use cases:
  For someone who doesn’t want to have to drag up the garden hose each time.
  Automated watering schedules
  Gathering data for a group of plants to get an idea of what conditions they prefer.
  Water different garden areas based on plant needs.

## Slide 4: Design
Start off with the basics
  Detect soil moisture
  Detect temperature and humidity
  Create a basic menu system (displayed with i2c LCD)

## Slide 5: Factors that influence moisture sensor readings
The amount of water given to the plant
  More water = higher moisture readings
Soil type
  Higher drainage = greater moisture drop
Environmental
  More light or heat = greater moisture drop

## Slide 6: Problems
The less deeper the soil moisture sensor = the lower the moisture reading
  Having the sensor deeper could provide better readings
Low and high moisture readings can vary based on soil type
  Not really a consistent set range
Plants can have different watering needs
  Thus different moisture ranges

## Slide 7: Improvements
Add a water pump
Monitor water levels for that water pump
Add a light sensor
Add an addressable LED to convey plant health
Add a rain sensor
Possibly make a bigger menu system (scrap ISR and adding more buttons)
  Soil moisture menu
  Water levels menu
  Climate menu
  Light levels menu

## Slide 8: Breadboard layout

## Slide 9: Video demonstration

## Slide 10: Recording data